## Slide 1: Mct2 Automation
Notes: 1
1
1
1

## Slide 2: Cédric Lenoir
Cedric.Lenoir@hevs.ch
Bureau 23N.412

## Slide 3: Principes généraux
1- Assurance qualité
2- S-88 & PackML
3- IEC 61131-3
4- Réseau OT
5- OPC UA
6- Sécurité OT
7- Sécurité machine
8- HMI
9- Alarmes
10- Maintenance
11- Industrie 5.0
12- Decommissioning
Connaissance
Application
Jugement

## Slide 4
IEC 61131 structured text vs Java
  Target audience
  For people with previous knowledge of Java.
  In the context of HES-SO of Valais basis Inf1_2122 by Pierre-André Mudry.
public class MyProgram
{
//Program entry point
public static void main(String[] args)
{
int var1=3;
int var2=4;
var1 = var1 + var2;
}
}
DATA_BLOCK "DB_Learn"
NON_RETAIN
VAR
var1 : Int;
var2 : Int;
END_VAR
BEGIN
var1 := 3;
var2 := 4;
END_DATA_BLOCK
"DB_Learn".var1 :="DB_Learn".var1 + "DB_Learn".var2;
Notes: 4
4
4
4
4

## Slide 5: Cyclic Interrupt, Cyclic, Interrupt

## Slide 6: Interrupt vs Cyclic
IEC 61131
Java
Program starts once.
Standard programs are cyclic

## Slide 7: Types
IEC 61131
Bool 1 bit
Char 1 byte
WChar 2 byte
Byte 1 byte
Sint 2 byte
Int 4 byte
Dint 8 byte
Real 4 byte
LReal 8 byte
Java
boolean 1 bit
char 2 byte
byte 1 byte
short 2 byte
int 4 byte
long 8 byte
float 4 byte
double 8 byte
Not interesting to use short forms if processor has 64 bits…
Excepted, maybe for fast communication in real-time.

## Slide 8: Base 2 – 10 - 16
IEC 61131
Java
// Binary diVar1 = 0b101;
// Decimal
diVar2 = 1234;
// Hexadecimal
diVar3 = 0xAB34;
// Binary diVar1 := 2#101;
// Decimal
diVar2 := 1234;
// Hexadecimal
diVar3 := 16#AB34;
Note the difference for assignation
Java “=“ IEC -61131 “:=“

## Slide 9: Comments
// comments
Java
IEC 61131
// comments
/* comments */
/** * comments */
(*
other comments
*)

## Slide 10: Variable Scope
IEC 61131
The scope of a variable depends on the place of its declaration.
FB  Only in FB
FC Function  In Function
DB everywhere
OB in OB
Java
The scope of a variable starts at its declaration and ends when the block is finished.
In IEC 61131 the variable MUST be declared in a header. In TIA Portal in the “table”, which is a graphical representation of the header.

## Slide 11: Dynamic vs Static
IEC 61131
With IEC 61131-3 standard variables are static, they are defined before the program runs.
Java
With Java, standard variables are defined in the code, they are dynamic.
Static variables have declaration and instanciation in a Data Block DB
Not fully true, but out of the scope of this course.

## Slide 12: Arithmetic operators
IEC 61131
Java
// Multiplication
x = y * z;
// Addition
x = y + z;
// Subtraction
x = y - z;
// Division
x = y / z;
// Modulo
x = y % z;
// Multiplication
x := y * z;
// Addition
x := y + z;
// Subtraction
x := y - z;
// Division
x := y / z;
// Modulo
x := y % z;

## Slide 13: Increment operator
IEC 61131
Java
// Pre increment
x = ++y;
// Post increment
x = y++;
// Pre decrement
x = --y;
// Post decrement
x = y--;
// Pre increment
// does not exist
// Post increment
// does not exist
// Pre decrement
// does not exist
// Post decrement
// does not exist

## Slide 14: Assignation operators
IEC 61131
Java
// Addition short
x += y;
// Substration short
x -= y;
// …
// Addition short
// does not exist
// Substration short
// does not exist
// …

## Slide 15: Binary operators
Java
IEC 61131
// And
result = a & b;
// Or
result = a | b; // Shift Right
result = a >> 1;
// Shift Left result = a << 3;
// And
result := a AND b;
// Or result = a OR b;
// Shift Right result = a SHR 1;
// Shift Left result = a SHL 3;

## Slide 16: If… Else…
IEC 61131
Java
if(temp <= 0){
diSet = diHighPower}
else if(temp > 0 && temp < 15){
diSet = diMidPower;}
else{
diSet = diLowPower;}
IF "DB_L".temp <= 0 THEN
"DB_L".diSet := "DB_L".diHighPower;
ELSIF "DB_L".temp > 0 AND "DB_L".temp < 15 THEN
"DB_L".diSet := "DB_L".diMidPower;
ELSE
"DB_L".diSet := "DB_L".diLowPower;
END_IF;
;

## Slide 17: switch … case
IEC 61131
Java
switch (theSignal){
case RED:
diVelocity = 0;
break;
case ORANGE:
diVelocity = 30;
break;
case GREEN:
diVelocity = 50;
break;
default:
diVelocity = -1;
break;
}
CASE "DB_L".theSignal OF
1: // Red
"DB_L".diVelocity := 0;
2: // Orange
"DB_L".diVelocity := 30;
3: // Green
"DB_L".diVelocity := 50;
ELSE // Statement section ELSE
"DB_L".diVelocity := -1;
END_CASE;
Enum exists in standard definition of IEC 61131-3
Unfortunately, ENUM does not exist in TIA Portal.

## Slide 18: for … FOR
IEC 61131
Java
for (int i = 0; i < 15; i = i + 2){
theSignal++;
}
FOR "DB_L".iLoop := 1 TO 15 BY 2 DO
"DB_L".theSignal := "DB_L".theSignal + 1;
END_FOR;
I never use a variable with a single char like int i.
Because it is difficult to find in the code.
Try to search “i” in your code…
Use iLoop instead.

## Slide 19: while … WHILE DO
IEC 61131
Java
while (nCounter != 0) {
nVar1 = nVar1*2;
nCounter--;
}
WHILE nCounter <> 0 DO
nVar1 := nVar1*2
nCounter := nCounter-1;
END_WHILE;
If nCounter = 0, the code inside the loop is never executed.
Note: this example from Beckhoff website is bad ! Could conduct to infinite loop never write that do not use <> !!!

## Slide 20: do while … REPEAT UNTIL
IEC 61131
Java
int count = 1;
do {
nVar1 = nVar1*2
count++;
} while (count >= 11);
REPEAT
nVar1 := nVar1*2;
nCounter := nCounter+1;
UNTIL
// from the web = 11
nCounter >= 11
END_REPEAT;
The code inside the loop is executed at least once.
Note: One more time the example from the web was bad!!
But this time I changed it !!!

## Slide 21: continue … CONTINUE
IEC 61131
Java
for (int i = 0; i < 15; i = i + 2){
if (i < 5){
continue;
}
theSignal = 1;
}
FOR "DB_L".iLoop := 1 TO 15 BY 2 DO
IF ("DB_L".iLoop < 5) THEN
CONTINUE;
END_IF;
"DB_L".theSignal := 1;
END_FOR;

## Slide 22: break … EXIT
IEC 61131
Java
for (int i = 15; i >= 1; i = i - 2){
if (i < 5){
break;
}
theSignal = 1;
}
FOR "DB_L".iLoop := 15 TO 1 BY -2 DO
IF ("DB_L".iLoop < 5) THEN
EXIT;
END_IF;
"DB_L".diSet := 1;
END_FOR;

## Slide 23: enum
IEC 61131
Java
enum State{
OPEN, CLOSED, BROKEN
};
TYPE E_TrafficSignal :
(
eRed,
eYellow,
eGreen := 10
);
END_TYPE
;
Enum Exist in standard definition of IEC 61131-3
Unfortunately, ENUM does not exist in TIA Portal.

## Slide 24: Class vs Function Block
IEC 61131
Java
public class Rectangle{
int width;
int height;
int surface(){
return width * height;
}
int perimeter(){
return 2*width + 2*height;
}
}
FUNCTION_BLOCK "FB_Rectangle"
VAR_INPUT
diWidth : DInt;
diHeight : DInt;
END_VAR
VAR_OUTPUT
diSurface : DInt;
diPerimeter : DInt;
END_VAR
BEGIN
#diSurface := #diWidth * #diHeight;
#diPerimeter := 2 * #diWidth +
2 * #diSurface;
END_FUNCTION_BLOCK

## Slide 25: Function
IEC 61131
Java
public static int abs(int x) {
if (x > 0)
return x;
else
return -x;
}
FUNCTION "FC_abs" : DInt
VAR_INPUT
dix : DInt;
END_VAR
BEGIN
IF #dix > 0 THEN
#FC_abs := #dix;
ELSE
#FC_abs := - #dix;
END_IF;
END_FUNCTION
;
In TIA Portal, VAR_INPUT usually described in a graphical view, a table.
Text view available from V15.1
In TIA Portal, VAR_INPUT BEGIN and END_FUNCTION are hidden.
Un fonction en IEC 61131 est toujours statique !

## Slide 26: Class vs TYPE
IEC 61131 InOut
TYPE "Rectangle_typ"
STRUCT
diWidth : DInt;
diHeight : DInt;
diSurface : DInt;
diPerimeter : DInt;
END_STRUCT;
END_TYPE
FUNCTION_BLOCK "FB_Rectangle InOut"
VAR_IN_OUT
param : "Rectangle_typ";
END_VAR
BEGIN
#param.diSurface := #param.diWidth * #param.diHeight;
#param.diPerimeter := 2 * #param.diWidth +
2 * #param.diHeight;
END_FUNCTION_BLOCK
An IEC TYPE is a class without any code.
We can define a Function Block without variables. Passed by reference/address

## Slide 27: Instantiation
IEC 61131
Java
// Declaration
Rectangle room;
// Instanciation
room = new Rectangle();
// Use room.witdh = 10;
room.height = 4;
int s = room.surface();
// Declaration + Instanciation
DATA_BLOCK "FB_Rectangle_DB"
NON_RETAIN
"FB_Rectangle"
BEGIN
END_DATA_BLOCK
// Call
"FB_Rectangle_DB"(diWidth:=10,
diHeight:=4);
// Use
"DB_L".diS := "FB_Rectangle_DB".diSurface;
"DB_L".diP := "FB_Rectangle_DB".diPerimeter;
Java declaration + instantiation (reserve memory dynamically).
Instantiate memory in a DataBlock. Static memory
Call to compute internal code.
Function Bloc is a method, it does nothing if not called
Unlike Java, does not compute anything, no independent methods

## Slide 28: Class vs Function Block
IEC 61131
Java
Class need declaration and instantiation.
Instantiation is dynamic, while program is running.
Objects can have methods.
Function Block need declaration
Instantiation is static, made by automatically by the linker, BEFORE the start of the program.
Function Blocks is a Method. It must be run to compute internal values.

## Slide 29: Array
IEC 61131 (declaration)
Java
double[] marks = { 5, 5.5, 3.5, 4 };
double average = 0;
for (int i = 0; i < marks.length; i++) {
average = average + marks[i];
}
average /= marks.length;.
DATA_BLOCK "DBx"
VAR
marks : Array[0..3] of Real;
average : Real;
END_VAR
BEGIN
marks[0] := 5.0;
marks[1] := 5.5;
marks[2] := 3.5;
marks[3] := 4.0;
END_DATA_BLOCK
Declaration, usually done in graphical mode in TIA Portal

## Slide 30: Array
IEC 61131 code
Java
double[] marks = { 5, 5.5, 3.5, 4 };
double average = 0;
for (int i = 0; i < marks.length; i++) {
average = average + marks[i];
}
average /= marks.length;.
Damned !

## Slide 31: Array length in IEC 61131
IEC 61131
Use a constant to define the length(-1) of your array.

## Slide 32: Array length in IEC 61131
IEC 61131
// Note that For...Loop imposes a Int
"DBx".rAverage := 0;
FOR "DBx".iLoop := 0 TO UDINT_TO_INT("udiMyArraySizeNm1") DO
"DBx".rAverage := "DBx".rAverage +
"DBx".rMarks["DBx".iLoop];
END_FOR;
// Note the udiMyArraySizeNm1 is the size - 1
"DBx".rAverage := "DBx".rAverage / UDINT_TO_REAL("udiMyArraySizeNm1"+1);

## Slide 33: Dynamic Array length in IEC 61131
IEC 61131 specific to TIA Portal, CountOfElements
FUNCTION "FC_GetArraySize" : Void
VAR_OUTPUT
udiSize : UDInt;
END_VAR
VAR_IN_OUT
vPointer : Variant;
END_VAR
BEGIN
#udiSize := CountOfElements(#vPointer);
END_FUNCTION
"FC_GetArraySize"(vPointer := "DBx".rMarks, udiSize => "DBx".udiArrayLength);

## Slide 34: OB FB FC DB
IEC 61131

## Slide 35: DB
Memory
IEC 61131
A DB is an Object

## Slide 36: FB
Data
Function
Function Block
IEC 61131
A FB is a Class

## Slide 37: FB call options
Single instance
The function block saves its data in its own instance data block. (Create an instance)
Multi instance
It saves its data in the instance data block of the calling function block. (Create an instance)
Parameter instance
If you call the function block as a parameter instance, the function block saves its data in the instance you specify as block parameter.
InOut (Does not create an instance !)
IEC 61131

## Slide 38: In Out InOut
In := copy value to FB
Out => copy FB to value
InOut := pass reference to…, that is: address of a variable, structure or FB.
"FB_PPTX_DB"(myInputValue:="PPTX_DB".TheInputValue,
myOutputValue=>"PPTX_DB".TheOutputValue,
myInOutValue:="PPTX_DB".TheInOutStruct);
IEC 61131

## Slide 39: Static Temp Constant
IEC 61131

## Slide 40: FC
IEC 61131
A function is a FB without memory
That is: without instance.
From the point of view of a Java programmer, this is a Static Function

## Slide 41: Merci de votre attention